## Slide 1: Renewable Energy

## Slide 2: Presentation Overview
Your Presenter.
Typical Wind Farm Project.
Financial Overview.

## Slide 3: Your Presenter
Presenters Expertise
  Business Analysis,
    British Telecom (BT), UK & USA.
    (Inland Revenue) EDS, UK
  Senior Analyst,
    E.S.A, European Space Agency, Holland.
    Blackburn Associates, UK
    Unisys USA.
    (HSBC) Formerly Midland Bank, UK
  Responsibility
  All Technical Designs.
  Business Strategy.

## Slide 4: All about Carbon Emissions
Cost of Carbon Emissions
  EU Debating target reduction of CO2 by 30% by 2020.
  Power Station, Oil, Diesel, Coal.
  Vehicle, Hydrogen cell Vehicles and Hybrid vehicle.
  Global trade, cost of transport!!
  Global Communication, large carbon footprint.
    20 Emails per day size 1Mb = 20g CO2 per email.
    Per year 12kg CO2.
    Now how many emails are sent globally? 294 Billion per day, extrapolated based on 2010!!
  Consumer goods, Standby or Sleep both consume up to 80% of energy, new generation of consumer goods consume <1%

## Slide 5: Reduce CO2 Using Renewable Energy
Renewable Energy PV
  Photovoltaic-PV.
    Monocrystalline
      cells are cut from a single crystal of silicon- they are effectively a slice from a crystal.
      Efficiency 15%-17%
      Cost $0.90-$1.10 per watt
    Polycrystalline
      cells are effectively a slice cut from a block of silicon, consisting of a large number of crystals.
      Efficiency 14%-16%
      Cost $0.79-$1.00 per watt

## Slide 6: Reduce CO2 Using Renewable Energy
Renewable Energy PV
    Concentrated PV
      These systems are unique because sunlight is concentrated through a lens onto high performance solar cells, thus increasing the electricity generated.
      Efficiency 25%-40% in development
      Cost $4-$5 per watt
    Nano PV
      Compared to conventional solar cells, Nano PV’s solar cell manufacturing possesses one third of manufacturing cost, one third of number of process steps and nearly 300 times less amount of material consumption. These factors correspond to the lowest system cost.
      25% plus

## Slide 7: Reduce CO2 Using Renewable Energy

## Slide 8: Reduce CO2 Using Renewable Energy
Wind Turbines
  Wind Turbines.
    Hawt
      Horizontal-axis wind turbines (HAWT) have the main rotor shaft and electrical generator at the top of a tower, and may be pointed into or out of the wind.
      Energy Range 100w – 10mw
      Wind Class 1-7
      Industrial Class wind turbines Cut in 3m/s
      Industrial Class wind turbines Rated 10-13m/s
      Industrial Class wind turbine Cut Out 20-25m/s
      Rotor Diameter between 3m – 136m
      Tower Size from between 6m – 143m
      Swept Area as a guide 3 Time rotor diameter.

## Slide 9: Reduce CO2 Using Renewable Energy
Wind Turbines
  Wind Turbines.
    Vawt
      Vertical-axis wind turbines (VAWT) have the main rotor shaft vertical and electrical generator at the bottom.
      Energy Range 100w – 10kw
      Wind Class 1-7
      Industrial Class wind turbines Cut in 2m/s
      Industrial Class wind turbines Rated 9-12m/s
      Industrial Class wind turbine Cut Out 30+m/s
      Rotor Diameter between 3m – 6m
      Swept Area as a guide 2 Time rotor diameter.

## Slide 10: Reduce CO2 Using Renewable Energy
Wind Turbines Nacelle Type
  Synchronised.
    No Energy Required on Start up
  Asynchronous.
    Energy Required from the grid on Start up.
  Transmission Type.
    Direct Drive
    Gearbox

## Slide 11: Reduce CO2 Using Renewable Energy
Typical Wind Turbine Specification

## Slide 12: Reduce CO2 Using Renewable Energy
Typical Wind Turbine Specification

## Slide 13: New Generation Wind Turbines
Increased Capture of wind resource.
  3m/s Cut in speed
  Increase Tower Size up to 143m onshore
  Increase Rotor Size up to 128m onshore
  More Efficient Direct Drive Mechanism, Eliminated Gears.
  Increased wind Farm Annual Yield.
  Less Turbines required to produce the same yield
Financial Implications.
  Less Cover space.
  Less Construction Cost.
  Increased Availability Time.
  Reduced Maintenance Cost.
  Reduced Operational Cost.

## Slide 14: Desktop Software
EMD Wind Pro

## Slide 15: How did we Measure Wind
  70m High Mast Nexgen
  Sensors Placed 53m and 70m
  Sensors
    Vector A100LK Anemometer
    Vector W200P Potentiometer Wind Vane
    Setra Pressure Sensor Kit
    Thermistor
  Nomad 2 GSM Data logger

## Slide 16: EMD Wasp Wind Analyses Mast Data
Weibull Distribution
  Occurrence of wind speed in (%)
Energy Rose
  Wind Direction and Occurrence
  show KWh
Mean wind speed(m/s)
  Average wind Distribution
Frequency(%)
  Occurrence of wind speed against
  Direction
Conclusion
  53m wind reading 5.53-6.23m/s
  70m wind reading 6.04-6.82m/s
    Direction WNW-SSW

## Slide 17: EMD Wasp Wind Analyses 30 years Satellite Data
Weibull Distribution
  Occurrence of wind speed in (%)
Energy Rose
  Wind Direction and Occurrence
  show KWh
Mean wind speed(m/s)
  Average wind Distribution
Frequency(%)
  Occurrence of wind speed against
  Direction
Conclusion
  5.6 - 6.13m/s
  Direction W-SSW

## Slide 18: Wind Farm Main Results at 70m
Wind Speed
  5.7m/s
Energy Produced per Turbine
  4,892.8mw
Annual Yield
  At 43 Turbines 1.8mw
  210,390.4mw
Capacity Factor
  31%

## Slide 19: Legal Obligations
Cyprus Electricity Authority (EAC) Are Obliged to purchase all renewable energy produced.
  EU Law: Brussels, 02.07.2009 C(2009)5398, N 143/2009 – Cyprus
  “14. EAC will be obliged to buy all electricity produced in Cyprus from renewable sources and will carry out all administrative work related to the scheme, including the collection of the levy and the distribution of compensatory benefits to local authorities.”
  Current Purchase Price per KW is 14.5c

## Slide 20: Renewable Energy Status in Cyprus
Current Annual Electricity Needs: 1.2 GW/h
By 2016 the Annual Electricity Needs: 1.6 GW/h
EU Directive to Produce 20% (13%) of the Needed Energy via Renewable Energy by 2020: 500 MW/h
Currently Licences Issued Cover 166MW/H
Current Annual Yield Produced via Renewable Energy is: <1%

## Slide 21: Financial Overview
Project Plan
Project Construction Cost.
Operational Expenses.
Operational Income Impact.
Operational Income Overview.
Financial Summary.

## Slide 22: Summarised Project Plan (Prince 2)

## Slide 23: Project Construction Costs
Turbines | € 77,400,000
Infrastructure | 4,578,000
80MVA Transformers | 4,000,000
3.5MVA Transformers | 6,400,000
Land Purchase | 10,000,000
Consultancy | 192,000
Civil Engineer | 2,392,000
Electrical Engineer | 450,000
Architect | 500,000
Buildings Concrete Foundations | 240,000
Steel | 640,000
Wind Turbine Foundations | 960,000
Crane Rental | 600,000
Site Security | 65,000
Buildings | 450,000
Control Systems | 2,100,000
Precast Conduit | 360,000
Cabling Electrical Network | 990,000
Cabling Data Network | 80,000
Miscellaneous | 850,000
Total Construction Expenses | € 113,247,000

## Slide 24: Operational Expenses
 | 1st Year | 30th Year
Salary (Office & Overhead) | € 396,000 | € 534,550
Salary (Consultancy) | € 196,000 | € 250,000
Payroll (Social Security) | € 19,600 | € 33,455
Outside Services Security | € 40,000 | € 40,000
Supplies (Off and Operation) | € 30,000 | € 30,000
Repairs/ Maintenance | € 350,000 | € 3,105,034
Car, Delivery and Travel | € 4,000 | € 4,000
Accounting and Legal | € 20,000 | € 20,000
Telephone | € 3,600 | € 3,600
Utilities | € 18,000 | € 18,000
Insurance | € 1,543,450 | € 2,019,155
Land Rental | € 7,600 | € 7,600
Total Expenses | € 2,628,250 | € 6,065,393

## Slide 25: Operational Income Impact
Global Retail Fuel Index's 2007-2011
Global Inflation Rate Index 1971-2011
  Domestic Electricity Price Increase 12.9% between 2010-2011
  Domestic Electricity Price Increase 29.2% between 2007-2011
    Domestic Electricity Annual Average Price Increase 7.3% between 2007-2011
  Cyprus Domestic Electricity Annual Average Price Increase 10.33% between 2009-2011
Income Impact at a Conservative 0%, 2% & 3.05% increase Annually?

## Slide 26: Inflation and Fuel Index Increase
Chart: Inflation Increase Annually%
| 2011 | 2010 | 2009 | 2008 | 2007 | 2006 | 2005 | 2004 | 2003 | 2002 | 2001 | 2000 | 1999 | 1998 | 1997 | 1996 | 1995 | 1994 | 1993 | 1992 | 1991 | 1990 | 1989 | 1988 | 1987 | 1986 | 1985 | 1984 | 1983 | 1982 | 1981 | 1980 | 1979 | 1978 | 1977 | 1976 | 1975 | 1974 | 1973 | 1972 | 1971 | 1970
RPI Increase Annually% | 0.051875 | 0.045875 | -0.008625 | 0.043625 | 0.043375 | 0.0285 | 0.030375 | 0.02775 | 0.03025 | 0.012625 | 0.0215 | 0.02825 | 0.0165 | 0.036125 | 0.0285 | 0.024125 | 0.034375 | 0.024625 | 0.015375 | 0.04 | 0.067875 | 0.09075 | 0.079125 | 0.041625 | 0.041375 | 0.034875 | 0.063125 | 0.050375 | 0.04375 | 0.09775 | 0.11938 | 0.194 | 0.11487 | 0.084125 | 0.16988 | 0.17788 | 0.23375 | 0.1505 | 0.087625 | 0.0685 | 0.094625 | 0.057625
Chart: Fuel Price Index Increase 29.2%
| 2007 |  |  |  |  |  |  |  |  |  |  |  | 2008 |  |  |  |  |  |  |  |  |  |  |  | 2009 |  |  |  |  |  |  |  |  |  |  |  | 2010 |  |  |  |  |  |  |  |  |  |  |  | 2011 |  |  |  |  |  |  |  |
Fuel Price Index Increase 29.2% | 135.2 | 135.6 | 135.6 | 134.4 | 132.9 | 131 | 129.4 | 128.7 | 128.5 | 128.5 | 128.5 | 128.5 | 129 | 142.7 | 142.7 | 145.7 | 145.7 | 145.7 | 145.7 | 151.9 | 167.5 | 168.8 | 168.8 | 168.8 | 168.4 | 168.4 | 167.6 | 159 | 155.5 | 155.5 | 155.5 | 155.5 | 155.5 | 155 | 155 | 155 | 155 | 155 | 155 | 154.7 | 154.7 | 154.7 | 154.7 | 154.7 | 154.7 | 154.3 | 154.3 | 156.2 | 157.5 | 159.8 | 161 | 161 | 161 | 161 | 161 | 162.5 | 174.7

## Slide 27: Operational Income Impact
Income Impact at a Conservative 0%, 2% & 3.05% increase of the Price of KW Annually for 30 Years
Current Price of KW: 14.5 c
Based on a Average Wind Speed Constant at: 5.7 m/s
Excluding any adjustment due to altitude from 70m-120m

## Slide 28: Financial Summary
Operational Income comparison |  |  |  | 
 |  | Annual KW Price Increase of 0% | Annual KW Price Increase of 2% | Annual KW Price Increase of 3.05%
IRR (Internal Rate Of Return) |  |  |  | 
Gross |  | 20.90% | 23.25% | 24.45%
Net |  | 13.84% | 16.45% | 17.77%
NPV (Net Present Value) |  |  |  | 
6% |  | € 141,293,984 | € 243,071,316 | € 294,592,045
8% |  | € 141,293,984 | € 148,428,466 | € 206,795,197
10% |  | € 69,060,493 | € 120,492,149 | € 146,019,123
12% |  | € 47,345,893 | € 84,217,319 | € 102,865,684
PBP (Pay Back Period) |  | 6 Years 10 Months | 6 Years 8 Months | 6 Years 7 Months
Sales Balance (30 years) |  | € 738,300,411 | € 1,090,628,160 | € 1,295,334,289

## Slide 29: Income Comparison Overview
Duration - Years
Chart: 
Income- Annual Increase of 0% | 0 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7 | 24610013.7
Income- Annual Increase of 2% | 0 | 24610013.7 | 25102213.974 | 25604258.2535 | 26116343.4185 | 26638670.2869 | 27171443.6927 | 27714872.5665 | 28269170.0178 | 28834553.4182 | 29411244.4866 | 29999469.3763 | 30599458.7638 | 31211447.9391 | 31835676.8979 | 32472390.4358 | 33121838.2446 | 33784275.0094 | 34459960.5096 | 35149159.7198 | 35852142.9142 | 36569185.7725 | 37300569.488 | 38046580.8777 | 38807512.4953 | 39583662.7452 | 40375336.0001 | 41182842.7201 | 42006499.5745 | 42846629.566 | 43703562.1573
Income - Annual Increase of 3.05% | 0 | 24610013.7 | 25360926.743 | 26134752.0203 | 26932188.6413 | 27753957.0472 | 28600799.6616 | 29473481.5613 | 30372791.1674 | 31299540.9579 | 32254568.2014 | 33238735.7136 | 34252932.6371 | 35298075.2442 | 36375107.7651 | 37485003.2408 | 38628764.4021 | 39807424.576 | 41022048.6183 | 42273733.8768 | 43563611.1817 | 44892845.8679 | 46262638.8274 | 47674227.5947 | 49128887.4642 | 50627932.6429 | 52172717.4377 | 53764637.4785 | 55405130.9796 | 57095680.0386 | 58837811.9757

## Slide 30: Operational Income Margins
Thank You For Attending Any Questions?